## Slide 1: Indications for capnography in intubated patients receiving mechanical ventilation
Continuous monitoring of pulmonary ventilation
  Early detection of hypoventilation and hyperventilation, essential in neurological patients and elevated intracranial pressure
  Adjustment of tidal volume, respiratory rate, and minute ventilation
Confirmation and continuous monitoring of endotracheal tube position
  Detection of esophageal intubation, displacement, and accidental extubation
Identification of mechanical and obstructive alterations
  Capnogram morphology analysis: “shark fin,” auto-PEEP, asynchronies
Assessment of CPR quality and identification of return of spontaneous circulation
Estimation of physiological dead space, V/Q alterations, and PEEP titration
  P(a–et)CO2 gradient and ETCO₂ trend analysis
Detection of ventilator malfunction and endotracheal tube issues
  Circuit disconnection, tube obstruction, secretion accumulation
Notes: Figure 1. Indications and benefits of capnography integrated with mechanical ventilation waveforms in the intubated patient.

## Slide 2: Capnography in intubated patients receiving mechanical ventilation
PvCO2
PACO2
PaCO2
PECO2
Time (s)
Q Perfusion
V Ventilation
Mechanical
Ventilator
INSP.
EXP.
Capnograph
mainstream
CO2
mmHg
0
A
B
C
D
E
40 -
25 -
PaCO2
P(a-et)CO2
ETCO2
Normal capnogram – phases
Patient
37 -
A
B
I
II
III
IV
B
C
C
D
D
E
I Dead space
II Alveolar emptying
III Alveolar plateau
IV Inspiration
Expiration
VCO2
Metabolism
.
Notes: Figure 2. Diagram illustrating mainstream capnography applied to the artificial airway of an intubated patient. Exhaled CO₂ partial pressure (PetCO₂) results from the interaction between CO₂ production, determined by cellular metabolism, pulmonary perfusion (the hemodynamic component), and alveolar ventilation (the ventilatory component). Continuous measurement of PetCO₂ throughout expiration yields a time-based capnogram composed of four phases. Phase I corresponds to exhalation of dead space volume, reflecting the dead space to tidal volume ratio (VD/VT), during which PetCO₂ equals zero. Phase II represents the transition as alveolar gas begins to empty, characterized by a rapid rise in PetCO₂. Phase III corresponds to the alveolar plateau at end-expiration, where the ETCO₂ (or PetCO₂) value is obtained. The gradient between arterial and end-tidal CO₂ partial pressures, P(a–et)CO₂, typically ranges from 2 to 5 mmHg and becomes smaller as ventilation–perfusion (V/Q) matching approaches ideal homogeneity.

## Slide 3: Capnography in intubated patients receiving mechanical ventilation
PECO2
Mechanical
Ventilator
INSP.
EXP.
Capnograph
mainstream
Normal capnogram integrated with mechanical ventilation waveforms
A
B
B
C
C
D
D
E
A
B
C
D
E
I
II
III
IV
VD
VT
I Dead space
II Alveolar emptying
III Alveolar plateau
IV Inspiration
Notes: Figure 3. Capnogram waveforms integrated with volume-time and flow-time curves of an ICU mechanical ventilator, demonstrating the four capnographic phases. Phase I corresponds to the exhalation of the dead space volume (VD), with PetCO₂ equal to zero and the potential quantification of VD from the tidal volume (VT) curve. Phase II reflects the transition as alveolar gas is exhaled, with a rapid increase in PetCO₂. Phase III represents the alveolar plateau extending to end-expiration, when expiratory flow returns to zero, and PetCO₂ is measured immediately before Phase IV, the onset of inspiration. ETCO₂ (PetCO₂) is shown with a normal physiological gradient of approximately 2–5 mmHg relative to PaCO₂, presented here for didactic purposes. Waveforms and data generated using the Xlung simulator.

## Slide 4: Capnography in intubated patients receiving mechanical ventilation ↑ metabolism and CO₂ production
🌡️ 36oC
🌡️ 40oC
49
46
37
34
Volume
mL
CO2
mmHg
↑PECO2
Mechanical
Ventilator
INSP.
EXP.
Capnograph
mainstream
Temperature
VCO2
Fever
Sepsis
.
P(a-et)CO2
Normal
↑PaCO2
↑PeCO2
Patient
Notes: Figure 4. Capnography in intubated patients receiving mechanical ventilation under conditions of increased metabolism and CO₂ production.
Fever, sepsis, and other hypermetabolic states increase CO₂ production (V̇CO₂), resulting in higher mixed expired CO₂ values (PECO₂). When ventilation–perfusion matching is preserved, both PaCO₂ and ETCO₂ rise proportionally, maintaining a normal arterial-to-end-tidal CO₂ gradient [P(a–et)CO₂]. An increase in body temperature (36 °C vs. 40 °C) alters capnographic values. It elevates CO₂ levels without changes in the expiratory flow pattern, indicating that alveolar hypoventilation, the primary differential diagnosis, is not responsible for the observed changes. Waveforms and data generated using the Xlung simulator.

## Slide 5: Capnography in intubated patients receiving mechanical ventilation Alveolar hypoventilation due to reduced tidal volume
500ml
250ml
80
75
40
37
Volume
mL
CO2
mmHg
↑PECO2
Mechanical
Ventilator
INSP.
EXP.
Capnograph
mainstream
↑ PACO2
V Ventilation
Tidal Volume
↑PaCO2
↑PeCO2
P(a-et)CO2
Normal
Patient
Notes: Figure 5. Capnography in intubated patients receiving mechanical ventilation during alveolar hypoventilation secondary to tidal volume reduction. A decrease in tidal volume reduces alveolar ventilation and results in CO₂ retention, producing proportional increases in PaCO₂ and exhaled CO₂ partial pressure (PetCO₂). In the presence of preserved ventilation–perfusion matching, the P(a–et)CO₂ gradient remains within the physiological range. Integration of physiologically normal-shaped capnograms with volume-time curves demonstrating a reduction in exhaled tidal volume from 500 mL to 250 mL supports hypoventilation as the mechanism responsible for increased PaCO₂ and ETCO₂. Waveforms and data generated using the Xlung simulator.

## Slide 6: Capnography in intubated patients receiving mechanical ventilation Pulmonary hypoperfusion due to hemodynamic shock (↓ Cardiac Output)
6L/min
2L/min
48
35
39
37
Volume
mL
CO2
mmHg
P(a-et)CO2
Elevated
↓PECO2
Mechanical
Ventilator
INSP.
EXP.
Capnograph
mainstream
↓ PACO2
V Ventilation
Cardiac output
↑PaCO2
↓PeCO2
Q Perfusion
x
↑PaCO2
↑VD/VT
Patient
Notes: Figure 6. Capnography in intubated patients receiving mechanical ventilation during pulmonary hypoperfusion secondary to hemodynamic shock with reduced cardiac output.
A decrease in cardiac output results in impaired pulmonary perfusion and reduced CO₂ delivery to the alveoli, leading to lower exhaled CO₂ (ETCO₂) despite preserved or elevated arterial CO₂ (PaCO₂). This condition is associated with increased physiological dead space (VD/VT) and widening of the P(a–et)CO₂ gradient. Capnograms obtained under conditions of normal (6 L/min) and reduced (2 L/min) cardiac output demonstrate a marked reduction in ETCO₂ with unchanged mechanical ventilation, highlighting the predominantly hemodynamic contribution to the observed capnographic alterations. Waveforms and data generated using the Xlung simulator.

## Slide 7: Capnography in intubated patients receiving mechanical ventilation Airflow limitation with increased airway resistance and auto-PEEP
9
27
45
43
38
Flow
L/min
CO2
mmHg
↓PECO2
INSP.
EXP.
↑ PACO2
V Ventilation
Rva cmH2O.L.s
Q Perfusion
↑PaCO2
Auto-PEEP
↑ VD/VT
↑Rva
33
VD/VT
Auto-PEEP
↑PaCO2
↓PeCO2
Airflow limitation
Capnograph
mainstream
Patient
Mechanical
Ventilator
P(a-et)CO2
Elevated
Notes: Figure 7. Capnography in an intubated patient receiving mechanical ventilation with airflow limitation, increased airway resistance, and the development of auto-PEEP.
Increased airway resistance (Raw) promotes expiratory flow limitation, impairing complete lung emptying. This condition results in dynamic air trapping and the generation of auto-PEEP, evidenced by the inability of expiratory flow to return to zero before the onset of the next inspiratory cycle. Consequently, effective alveolar ventilation is reduced, leading to an increase in the dead space-to-tidal volume ratio (VD/VT). Capnography typically demonstrates reduced ETCO₂ values despite a concomitant rise in PaCO₂, reflecting alveolar hypoventilation associated with widening of the P(a–et)CO₂ gradient. The capnogram exhibits a progressive upward slope of Phase III, characteristic of the classic shark-fin pattern seen in airflow obstruction. At the same time, the flow-time waveform confirms the presence of auto-PEEP. Waveforms and data generated using the Xlung simulator.

## Slide 8: Capnography in intubated patients receiving mechanical ventilation Recovering respiratory muscle effort after NMB
37
Flow
L/min
CO2
mmHg
EtCO2
P(a-et)CO2
Variables
PECO2
Mechanical
Ventilator
INSP.
EXP.
Capnograph
mainstream
34
*Ineffective efforts
38
*
*
*
Curare “clefts"
Notes: Figure 8. Diagram illustrating ineffective inspiratory efforts, visible on the flow waveform, and their corresponding effects on the capnogram. In this example, waveforms were generated by simulating reduced inspiratory muscle effort, as may occur during partial recovery from neuromuscular blockade (curare cleft). These events may occur near end-expiration, producing transient entrainment of CO₂-free gas, thereby altering PetCO₂ and potentially affecting ETCO₂ measurements. Consequently, variations in the P(a–et)CO₂ gradient may also be observed. NMB: neuromuscular blockade. Waveforms and data generated using the Xlung simulator.

## Slide 9: Capnography in intubated patients receiving mechanical ventilation Progression to cardiac arrest
Flow
L/min
CO2
mmHg
EtCO2
Rapid decline to zero
PECO2
INSP.
EXP.
38
CPR→
Capnograph
mainstream
Mechanical
Ventilator
Notes: Figure 9. Capnography in an intubated patient receiving mechanical ventilation during progression to cardiorespiratory arrest (CRA). As severe and rapidly progressive hemodynamic deterioration occurs, with abrupt reduction in cardiac output, pulmonary perfusion collapses, leading to a marked reduction in CO₂ delivery to the alveoli. Consequently, ETCO₂ rapidly declines toward near-zero values despite preservation of the ventilatory pattern, as evidenced by the maintained flow-time waveform.

## Slide 10: Capnography in intubated patients receiving mechanical ventilation Cardiopulmonary resuscitation until ROSC after cardiac arrest
CO2
mmHg
Flow
L/min
Initiation of CPR
EtCO2
- Reflects the quality of chest compressions
- Identifies the return of spontaneous circulation
ROSC
Ok
Weak
Strong
EtCO2
Target range
Notes: Figure 10. Capnography in an intubated patient receiving mechanical ventilation during cardiopulmonary resuscitation, from cardiopulmonary resuscitation (CPR) through initiation of chest compressions to return of spontaneous circulation (ROSC). During CPR, ETCO₂ values directly reflect pulmonary blood flow generated by chest compressions and serve as an indirect marker of compression quality. Ineffective compressions are associated with low ETCO₂ values, whereas more effective compressions produce progressive increases in ETCO₂ within the target range. A sustained and abrupt rise in ETCO₂ represents the classic indicator of ROSC. Flow-time waveforms demonstrate maintenance of ventilatory pattern throughout resuscitation, with oscillations related to chest compressions. At the same time, the capnogram shows the transition from low exhaled CO₂ levels during CPR to higher, more stable values after ROSC. Waveforms and data generated using the Xlung simulator.

## Slide 11: Capnography in intubated patients receiving mechanical ventilation Effect of PEEP on respiratory mechanics and P(a–et)CO₂ in ARDS
CO2
mmHg
Airway
Pressure cmH2O
P(a-et)CO2
15,5cmH2O
12cmH2O
14cmH2O
PaCO2
PeCO2
Driving
Pressure
cmH2O
44
38
48
40
42
39
Alveolar overdistension
↑VD/VT
and/or ↓ perfusion
Alveolar Recruitment
↓ VD/VT
and/or ↑ perfusion
↑
↑
PEEP: 15cmH2O
PEEP: 10cmH2O
PEEP: 5cmH2O
Notes: Figure 11. Capnography in an intubated patient with Acute Respiratory Distress Syndrome (ARDS) receiving mechanical ventilation in volume-controlled ventilation (VCV) mode with tidal volume set at 6 mL/kg predicted body weight during decremental PEEP titration (15 → 10 → 5 cmH₂O). A PEEP level of 10 cmH₂O resulted in the lowest driving pressure and the smallest P(a–et)CO₂ gradient, findings consistent with reduced pulmonary overdistension and greater alveolar aeration and/or improved ventilation–perfusion (V/Q) matching compared with the other tested PEEP levels. Waveforms and data generated using the Xlung simulator.

## Slide 12: Capnography in intubated patients receiving mechanical ventilation Findings Associated with Ventilatory Support Problems
CO2
mmHg
PiCO2 > 0
A) Rebreathing Due to Expiratory Valve Malfunction
CO2
mmHg
B) Air Leak
Volume
Leak
Time
Notes: Figure 12. Capnography in intubated patients receiving mechanical ventilation with abnormalities in the control of inspiratory and expiratory gas flow within the ventilator circuit.
In A) CO₂ rebreathing caused by expiratory valve malfunction results in partial return of exhaled gas at the onset of inspiration (Phases IV and I of the capnogram). An increase in inspired CO₂ partial pressure is observed (PiCO₂ > 0), proportional to the severity of rebreathing. In the absence of compensatory hyperventilation, PetCO₂ may also increase. In B) the presence of a circuit leak causes early reduction in PetCO₂, preventing the formation of the alveolar plateau and generating a characteristic capnogram morphology.

## Slide 13: Capnography in intubated patients receiving mechanical ventilation Findings Associated with Endotracheal Tube Problems
CO2
mmHg
A) Esophageal Intubation
CO2
mmHg
B) Endobronchial Intubation
Endotracheal Tube Repositioned
in the Trachea
Notes: Figure 13. Capnography in intubated patients receiving mechanical ventilation.
In A) esophageal intubation is characterized by extremely low or absent PetCO₂ values, sometimes displaying small transient waveforms due to residual CO₂ within the upper gastrointestinal tract immediately after intubation, followed by a flat tracing. The expression “no trace, wrong place” has been proposed to emphasize the urgency of immediate corrective action. In B) migration of the distal end of the endotracheal tube into the right main bronchus produces asymmetric lung emptying, resulting in a biphasic capnogram morphology. This pattern is typically corrected following appropriate repositioning of the tube within the trachea.

## Slide 14
↑Metabolic rate and/or hypoventilation
CO₂ rebreathing
Return of spontaneous circulation (ROSC) during CRA
Alveolar overdistension
↑ Excessively high PEEP
↓EtCO2
↑EtCO2
Capnographic Findings in Intubated Patients Receiving Mechanical Ventilation
www.xlung.net
Esophageal intubation or circuit disconnection
Air leak
Cardiorespiratory arrest
Shock or pulmonary embolism
Airflow obstruction
Notes: Figure 14. Summary of the main clinical conditions and their corresponding capnographic findings discussed in this chapter.